## Slide 1: TANGO GATOR-SAT Project
System Design Review
Naomi Camargo, Shadalou Fernandez, Andre Hada, Nicholas Hirsh, Nicholas Kottas, Dhruv Mathuria, Nishtha Rajani, Noah Touchton, Ian Truelsegaard
University of Florida – EAS4700 - October 9th, 2025

## Slide 2: Communications
Noah Touchton

## Slide 3: System Overview
One onboard computer in the main satellite manages data handling, with a 64GB eMMC for buffering payload data prior to downlink.
The communication system has dedicated subsystems for downlink, telemetry and command, and inter-sat links.
Data Handling
  Controlled by STM32H723VET6 microcontroller.
  Buffered on a SDINBDG4-64G-ZA3 eMMC.
Payload Downlink
  Downlink
Telemetry & Command
  System
Inter-Sat Communication
  System
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF

## Slide 4: Requirements
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF
Standard | Source | Name | Description | Supported By | Status
ASD-GTRS-020 | EAS 4700 Project Requirements | Communication System Capability | he GATOR-SAT SmallSat shall be able to receive commands and transmit image, health, and status data directly to Earth ground stations within sight of the spacecraft along its orbital path. | The S-Band antenna and transmitter | Complete
ASD-GTRS-018 | EAS 4700 Project Requirements | Maximum Mission Duration | The GATOR-SAT SmallSat shall have sufficient fuel to support observation operations and maintain the orbit for six months, not including transit time to/from the target orbit for the initial proof-of-concept mission. |  | Complete

## Slide 5: Derived Requirements
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF
Standard | Source | Name | Description | Supported By | Status
COM-GTRS-01 | ASD-GTRS-020 | Downlink Data System | The spacecraft shall provide access to payload and housekeeping data through a high-rate S-Band link. |  | 
COM-GTRS-02 | ASD-GTRS-020 | Data Buffering | The spacecraft shall store ≥7 days (≈2 GB) of data in case of missed passes. |  | 
COM-GTRS-03 | ASD-GTRS-020 | InterSat Crosslink Rate | The spacecraft shall support intersatellite communications at ≥100 kbps, enabling data relay and coordination. |  | 
COM-GTRS-04 | ASD-GTRS-020 | TT&C Link | The spacecraft shall maintain a continuous S-Band TT&C link at ≥9.6 kbps for health/status telemetry and command reception. |  | 
COM-GTRS-05 | COM-GTRS-01 | Daily Data Volume | The spacecraft shall downlink at least 288 MB per day to satisfy payload science return. |  | 

## Slide 6: Derived Requirements
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF
Standard | Source | Name | Description | Supported By | Status
COM-GTRS-06 | COM-GTRS-01 | Downlink Rate | The S-Band transmitter shall support a downlink rate sufficient to clear the required 288 MB within available ground station passes , |  | 
COM-GTRS-07 | COM-GTRS-01 | Ground Contact Utilization | The spacecraft shall transmit stored data during at least 2 ground station passes per day, leaving one additional pass margin. |  | 
COM-GTRS-08 | ASD-GTRS-018 | Lifetime Operations | The communications subsystem shall maintain functional capability for at least six months without hardware degradation that prevents required data return. |  | 
COM-GTRS-09 | COM-GTRS-01 | Link Redundancy | The comms subsystem shall include two independent paths: a high-rate downlink (PULSAR-STX) and a low-rate TT&C fallback (AX100). |  | 
COM-GTRS-10 | COM-GTRS-01 | Frequency Allocation Compliance | The S-Band system shall operate strictly within the 2.0–2.3 GHz CubeSat allocation to ensure regulatory compliance. |  | 

## Slide 7: Derived Requirements
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF
Standard | Source | Name | Description | Supported By | Status
COM-GTRS-11 | COM-GTRS-01, COM-GTRS-04 | Antenna Configuration | The spacecraft shall use a nadir-facing S-Band patch antenna for Earth link and two omnidirectional whips for crosslinks. |  | 
COM-GTRS-12 | COM-GTRS-02 | Data Prioritization | The onboard C&DH system shall prioritize transmission of housekeeping + health data before payload data in the event of bandwidth limitations. |  | 
COM-GTRS-13 | ASD-GTRS-020 | Data Formatting Standard | The spacecraft shall package payload and housekeeping data in a standardized frame structure (header, payload, checksum) so that ground stations can parse data consistently and in the correct sequence. |  | 
COM-GTRS-14 | ASD-GTRS-020 | Data Source Authentication | The spacecraft shall implement a method to verify that all uplinked commands originate from authorized ground stations, preventing unauthorized tampering. |  | 
COM-GTRS-15 | ASD-GTRS-020 | Data Receipt Confirmation | The spacecraft shall support a positive acknowledgment protocol (ACK/NACK) to confirm that transmitted frames are received correctly by the ground system. |  | 

## Slide 8: Derived Requirements
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF
Standard | Source | Name | Description | Supported By | Status
COM-GTRS-16 | COM-GTRS-13 | Sequential Data Ordering | The spacecraft shall include frame counters or time tags in each transmission so the ground station can verify that data is received in the correct order without loss or duplication. |  | 
COM-GTRS-17 | COM-GTRS-02 | Data Storage | The spacecraft shall have enough onboard storage to store the buffered data. |  | 

## Slide 9: Microcontroller Trade Study
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF

## Slide 10: Downlink Antenna Trade Study
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF

## Slide 11: Transceiver Trade Study
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF

## Slide 12: Transmitter Trade Study
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF

## Slide 13: InterSat Antenna Trade Study
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF

## Slide 14: InterSat Transciever Trade Study
Noah Touchton – ntouchton@ufl.edu
10/09/25
TANGO SDR​ - UF

## Slide 15: Requirements
Name - Email
10/09/25
TANGO SDR​ - UF
Req # | Description | System | Verification Method | Status
COM-GTRS-01 | The GATOR-SAT SmallSat shall be capable of launching either as a Co-manifested Payload (CPL) or primary payload on a suitable government-owned or commercially owned launch vehicle that can accommodate SmallSats. | All | Demonstration | 

## Slide 16: Requirements
Name - Email
10/09/25
TANGO SDR​ - UF
Req # | Description | System | Verification Method | Status

## Slide 17: Risk Template
ID | Risk | L | S | Mitigation
LIKELIHOOD | 5 |  |  |  |  | 
 | 4 |  |  |  |  | 
 | 3 |  |  |  |  | 
 | 2 |  |  |  |  | 
 | 1 |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5
 |  | SEVERITY |  |  |  | 
Name - Email
10/09/25
TANGO SDR​ - UF